## Slide 1: LAStools – de la DSM la DTM
Seminar "Soluții libere open source pentru prelucrarea și reprezentarea datelor geospațiale"
15-16 aprilie 2016 - Cluj-Napoca
Corina-Maria Ristea
Cristina Andra Vrînceanu
Ștefania-Alexandra Oancea

## Slide 2: Definiții
LAStools – o serie de instrumente pentru vizualizarea, procesarea și analiza fișierelor de tip .las (precum date LiDAR sau nor de puncte 3D rezultat în urma procesării imaginilor aeriene). http://rapidlasso.com/lastools/
DSM (Digital Surface Model) – modelul digital al suprafeței
DTM (Digital Terrain Model) – modelul digital al terenului
Sursa foto: www.simactive.com
DSM
DTM

## Slide 3: Date LiDAR vs. Nor de puncte 3D

## Slide 4: LAStools

## Slide 5: Configurare QGIS
Processing  Options  Providers  Tools for LiDAR data

## Slide 6
Articol DSM  DTM

## Slide 7: Flux de lucru – obţinere DTM

## Slide 8: Flux de lucru pentru obținerea DTM
INPUT
- nor de puncte/date LiDAR: .las/.laz
1. LASSORT
- output: .las/.laz
2. LASGROUND
- output: .las/.laz
3. LAS2DEM
-output: .tiff/alte formate

## Slide 9: 1. Lassort
Parametri
Notes: sorts the points of a LAS file into z-order arranged cells of a square quad tree and saves them into LAS or LAZ format. This is useful to bucket together returns from different swaths or to merge first and last returns that were stored in separate files.

## Slide 10: 2. Lasground
Parametri
Notes: is a tool for bare-earth extraction: it classifies the LiDAR points into ground points (class = 2) and non-ground points (class = 1). The tools works very well in natural environments such as mountains, forests, fields, hills, and even steep terrain but also gives excellent results in towns or cities.

## Slide 11
Rezultat lasground

## Slide 12: 3. Las2dem
Parametri
Notes: is a tool that triangulates LIDAR points from the LAS/LAZ format (or some ASCII format) into a temporary TIN and then rasters the TIN to create a DEM. The tool can either raster the ‘-elevation’, the ‘-slope’, the ‘-intensity’, the ‘-rgb’ values, or a ‘-hillshade’ or ‘-gray’ or ‘-false’ coloring. The output is either in BIL, ASC, IMG, FLT, XYZ, DTM, TIF, PNG or JPG format.

## Slide 13: Interfaţă LAStools

## Slide 14: Linii de comandă

## Slide 15: Rezultate

## Slide 16: Test Elveția
DSM
DTM

## Slide 17
Zonă de test LAStools
DSM
DTM

## Slide 18
Zonă de test LAStools
DSM
DTM

## Slide 19: Test Bâscenii de Sus, Buzău
DSM
DTM

## Slide 20
Input nor de puncte
DSM
Output lasground
DTM
Flux

## Slide 21: Întrebări…

## Slide 22: Vă mulțumim!